X-ray Safety

Quiz booklet designed to test your understanding of the MS Powerpoint Slide presentation

Quiz for Slide Show 1

1. The bremsstrahlung process produces x-rays when

- electrons are slowed in the cathode

- a vacancy in an electron orbital is filled

- a vacancy in the nucleus is filled

- electrons are stopped in the anode

  - Characteristic radiation is produced when

- electrons are slowed in the cathode

- a vacancy in an electron orbital is filled

- a vacancy in the nucleus is filled

- electrons are stopped in the anode

  - About ____ percent of the projectile electron energy is converted to x-ray energy

  - 1

  - 10

  - 25

  - 99

  - X-ray tubes filter out

- low energy electrons

- high energy electrons

- low energy x-rays

- high energy x-rays

  - Interactions that produce x-rays in the anode include

  - coherent

  - Compton

  - Bremsstrahlung

  - Pair production

  - Characteristic

    - 1, 3 and 5

    - 2 and 4

    - 3 and 5

    - 1, 2, 3, 4 and 5

  - The voltage applied to the x-ray tube is the

    - kVp

    - keV

7. Tungsten has the following binding energies

| Shell | K | L | M | N |
| --- | --- | --- | --- | --- |
| Energy (keV) | 69 | 11 | 2 | 1 |

Projectile electrons must have an energy of at least ____keV to produce K characteristic x-rays from tungsten

- 50

- 70

- 67

- 58

8. More than ____ percentage of an x-ray beam is made up of photons produced by the bremsstrahlung process

- 1

- 10

- 80

- 99

9. The energy of the individual photons is known as the

- kVp

- keV

10. Bremsstrahlung produces a ______ energy spectrum

- discrete

- continuous

11. Characteristic x-ray production produces a ______ energy spectrum

- discrete

- continuous

# Quiz to Slide Show 2

# In Questions 1.to 6 match the different x-ray spectra with the corresponding change

1.   _____  mA increase

2.   _____  mA decrease

3.   _____  kVp increase

4. _____  kVp decrease

5. _____ Filtration increase

6. _____ Filtration decrease

7. Changing ____ will change the energy of the characteristic radiation

  - mA

  - kVp

  - filtration

  - anode material

- 1, 2, 3, 4

- 4

- 2

- 1, 2, 3

8. Changing ____ will change the E max

  - mA

  - kVp

  - filtration

  - anode material

- 1, 2, 3, and 4

- 4

- 2

- 1, 2, and 3

Use the figure below for Questions 9 to 13

9. The average energy of this beam is

- 30 keV

- 70 keV

- 90 keV

- 90 kVp

- The maximum energy of this beam is

- 30 keV

- 70 keV

- 90 keV

- 90 kVp

- The energy of the characteristic x-rays is

- 30 keV

- 70 keV

- 90 keV

- 90 kVp

- The applied voltage that produced this beam is

- 30 keV

- 70 kVp

- 90 keV

- 90 kVp

13.The energy of the projectile electrons that produced this beam is

- 30 keV

- 70 keV

- 90 keV

- 90 kVp

Quiz to Slide Show 3

1. What is (are) the products of Compton Scattering?

- Electron

- Electron and scattered x-ray

- Electron and positive electron

- Scattered x-ray

For Questions 2 to 8 answer A for true and B for false

2. Bone has a higher x-ray attenuation than muscle because bone has a higher atomic number than muscle.

3. Bone has a higher x-ray attenuation than muscle because bone has a higher density than muscle.

4. X-ray attenuation depends on tissue thickness

5. In diagnostic x-ray applications where x-rays less than 100 keV are used, coherent scattering, Photoelectric effect and Compton scattering will be the only interactions between incident x-rays and patient tissue

6. Photodisintegration will be a commonly occurring interaction in x-rays within X-ray diffraction equipment .

7. Compton Scattering increases with atomic number.

8. Compton Scattering becomes a more dominant interaction with x-rays with an energy of greater than 26 keV.

9. Photoelectric interaction

- involves changes in energy and direction

- involves complete absorption of the photoelectron

- involves complete absorption of the incident x-ray

- requires at least 1.02 MeV

10. What is (are) the product (s) of photoelectric interactions?

- An electron

- An electron and a scattered x-ray

- A positron and a negatron

- A photoelectron and characteristic radiation

11. _____ is more likely in the case of 40 keV x-rays incident on soft tissue

- Coherent scattering

- Photoelectric effect

- Compton scattering

- Characteristic radiation

12. Compton Scattering

- involves scattering from the atomic nucleus

- involves complete absorption of the incident x-ray

- involves a change in direction with no change in energy

- involves scattering of x-ray from outer shell electrons

13. Exit radiation is made up of ______ radiation

- absorbed and scattered

- absorbed and transmitted

- scattered and transmitted

14. The HVL is the amount of material required to reduce the

- exit thickness to one-half the intensity

- exit intensity to one-half the thickness

- exit intensity to one-half the original intensity

- original intensity to one-half the exit intensity

15. The x-ray interaction that involves no loss of energy or ionisation is

- coherent

- photoelectric

- Compton

- Pair production

- Photodisintegration

Quiz to Slide Show 4

1. The background radiation in New Zealand is about _____ mSv per year

- 0.5

- 1.2

- 1.8

- 2.4

- 3.0

2. The maximum allowable effective dose to a radiation worker is _____ mSv per year

- 5

- 20

- 100

- 150

3. Alpha, gamma and x ray radiation have an LET and radiation weighting factor of _______ respectively

    - 10, 1, 1

    - 20, 2, 1

    - 20, 1, 1

    - 20, 5, 5

4. The components of NATURAL radiation are:

  - Cosmic radiation

  - medical radiation

  - terrestrial radiation

  - internal radiation

- 1, 2, 3 and 4

- 1, 2 and 3

- 2, 3 and 4

- 1, 3 and 4

5. The maximum allowed effective dose to the general public is ____ mSv per year

- 1

- 5

- 15

- 50

6. The unit of measure of exposure is the

- Roentgen

- Rad

- Gray

- Sievert

7. The SI unit of measure of dose is the

- Roentgen

- rad

- Gray

- Sievert

8. The SI unit of measure of effective dose is the

- rem

- rad

- Gray

- Sievert

9. The Equivalent Dose is the multiple of the

- Exposure and radiation weighting factor

- Dose and radiation weighting factor

- Dose and tissue weighting factor’

- Exposure and dose

10. The radiation weighting factor

- is roughly equivalent to the LET

- indicates the radiosensitivity of various organs

- is related to the exposure

- never exceeds a numerical value of 2

11. A 0.5 Gray dose of x-ray radiation is roughly equivalent to an effective dose of

- 0.5 Gray

- 0.5 Sieverts

- 1.0 Sieverts

- 10 Sieverts

# For questions 12 to 14 answer A for true and B for false

12. GM probes and dosimeters can be used to measure leakage and scatter from x-ray apparatus.

13. The reading from GM probes can used to obtain a reading for effective dose.

14. The Sievert is a measure of Equivalent Dose and Effective Dose

Quiz for Slide Show 5

1. ALARA means

- As low as readily achievable

- Always low and readily accessible

- Always low and really achievable

- As low as reasonably achievable

2. Which of the following is not a requirement for SAFE use of X-ray equipment

- Operators must be trained in safe use of the X-ray machine

- X-ray leakage and scatter must be measured periodically

- Safety interlocks are checked regularly

- Machine must have current licence holder.

3. X-ray diffraction equipment:

    - operated at low voltages but the intensity of x-rays can be high

    - operated at high voltages and high amperages

    - are always fitted with safety interlocks to prevent operator sustaining serious injury

4. Which of the following is most relevant to safe operation of X-ray diffraction equipment:

        - Reduce time spent next to machine

        - Follow manufacturer's instructions as well as verifying interlocks functioning and shielding is adequate

        - Increase distance away from machine

        - Logging all repairs

5. The NRL Safe Code of Practice:

              - Is designed as another revenue gathering exercise

              - Restates basic safety and ensures there is appropriate documentation

              - Is just another compliance document

# Text boxes

1

x-ray energy

Intensity

Question 4

Intensity

2

1

Question 3

2

1

x-ray energy

Intensity

Question 2

Intensity

2

1

x-ray energy

Question 1

2

1

x-ray energy

Intensity

2

1

x-ray energy

Intensity

2

Question 6

Question 5

30 keV

70 keV

90 keV